## Slide 1
KONERU LAKSHMAIAH EDUCATION FOUNDATION • KLEF
4-Bit Binary-to-Decimal
Converter and Display System
Digital Design using Logic Gates • DDCA • Course 26EC1202
PROJECT TEAM MEMBERS
S. Manikanta
2620040001
P. Vignesh
2620030101
S. Ram Charan
2620030241
S. B. Praveen
2620080019
Project Guide: Dr. Venkanna Isampalli • Department of Freshman Engineering
FINAL CAPSTONE DEMONSTRATION | ACADEMIC YEAR 2026–27

## Slide 2
01 • PROJECT OVERVIEW
Introduction and Objectives
2 / 6
The problem
A 4-bit binary input can represent 0–15. A single BCD display decoder cannot directly show every 4-bit value as a decimal number.
Our approach
Convert the 4-bit input into two BCD digits: tens and units, then send each digit to its own seven-segment display.
Project objective
Build and test a combinational logic circuit that displays decimal values 00–15 without a microcontroller.
HOW THE DATA FLOWS
4-bit input
B3 B2 B1 B0
Binary → BCD
Tens + Units
BCD drivers
Two decoders
Displays
00–15
Expected result: every input pattern from 0000 through 1111 maps to its decimal value, including the boundary transition from 9 to 10.

## Slide 3
02 • BOOLEAN LOGIC AND GATE FUNCTIONS
Theory and Logic Circuit
3 / 6
BASIC LOGIC GATES
NOT
Y = Ā
Inverts one input.
AND
Y = A·B
1 only when both inputs are 1.
OR
Y = A + B
1 when at least one input is 1.
XOR
Y = A ⊕ B
1 when inputs differ.
NAND
Y = ¬(A·B)
Complement of AND.
NOR
Y = ¬(A+B)
Complement of OR.
CONVERSION LOGIC (B3 MSB … B0 LSB)
T = B3(B2 + B1)
T = 1 for input values 10–15; otherwise T = 0.
U3 = 0 U2 = B2·¬B3 + B2·B1
U2 is the 4's bit of the units digit.
U1 = ¬B3·B1 + B3·B2·¬B1
U0 = B0
T is the tens digit's 1-bit BCD value. The units output is U3 U2 U1 U0. NOT gates provide complemented signals; AND/OR combinations implement the equations.
A combinational circuit has no stored state: the output is determined by the current input combination.

## Slide 4
03 • IMPLEMENTATION ARCHITECTURE
Circuit Design in Logisim Evolution
4 / 6
BUILD THE SYSTEM AS FOUR CONNECTED BLOCKS
INPUTS
4 switches
B3 B2 B1 B0
LOGIC CORE
NOT + AND + OR
Binary → BCD
TENS DECODER
BCD input: 000T
7-segment driver
UNITS DECODER
BCD input: U3U2U1U0
7-segment driver
TENS DISPLAY
Shows 0 or 1
UNITS DISPLAY
Shows 0–9
EXAMPLE: INPUT 1111₂ = DECIMAL 15
Tens BCD = 0001 • Units BCD = 0101 • Display = 15
In Logisim Evolution, use input pins/switches, gates, splitters if needed, and two seven-segment displays. Add a decoder block or build its logic explicitly.

## Slide 5
04 • VERIFICATION
Simulation Results and Truth Table
5 / 6
EXPECTED INPUT–OUTPUT MAPPING
Decimal | B3 B2 B1 B0 | Tens BCD | Units BCD | Display
0 | 0000 | 0000 | 0000 | 00
5 | 0101 | 0000 | 0101 | 05
9 | 1001 | 0000 | 1001 | 09
10 | 1010 | 0001 | 0000 | 10
12 | 1100 | 0001 | 0010 | 12
15 | 1111 | 0001 | 0101 | 15
TEST PLAN
Toggle all 16 input patterns (0000–1111) and compare both display digits with the expected decimal value.
BOUNDARY CHECK
Check 1001₂ = 09 and 1010₂ = 10. This verifies the conversion changes correctly after decimal 9.
Note: The table gives expected functional results. Replace/add actual Logisim screenshots after running the circuit in your installed version.

## Slide 6
05 • WRAP-UP
Conclusion and Applications
6 / 6
Outcome
A combinational logic design maps all 16 possible 4-bit inputs to decimal values 00–15 using BCD and dual-digit display stages.
Applications
Digital counters, measurement instruments, calculator displays, embedded panels, and teaching digital logic.
Future improvements
Reduce gate count with K-map minimization, add a fully verified Logisim testbench, and extend the design to larger input widths.
KEY TAKEAWAY
Logic gates provide the conversion logic; BCD decoder/driver stages translate each decimal digit into the seven-segment pattern.
Thank you • Questions and discussion