## Slide 1
COURSE CODE: 26EC1202E
CAPSTONE DIGITAL LOGIC PROJECT
4-Bit Binary to Decimal Converter Using Logic Gates
Synthesizing positional binary inputs (0000–1111) into dual-digit decimal readouts (00–15) through K-map optimization, MSI decoders, and TTL hardware realization.
KONERU LAKSHMAIAH EDUCATION FOUNDATION
Department of Freshman Engineering / Department of ECE • Academic Year: 2026–27
PROJECT TEAM MEMBERS:
PROJECT GUIDE:
Dr. Venkanna Isampalli
Department of Freshman Engineering
Manikanta
2620040001
Vignesh
2620030101
Ram Charan
2620030241
Praveen
262008019

## Slide 2
SECTION 01 • BACKGROUND & MOTIVATION
Introduction
Human-Machine Numeric Interface
Digital Computing Core: Microprocessors, ALUs, and registers process pure binary words (0s and 1s).
Human Readability: Humans naturally interpret information in standard base-10 decimal numerals.
Conversion Gap: 4 bits yield 16 binary patterns ($0000_2$ to $1111_2$) corresponding to decimal values 0 through 15.
Hardware Focus: Implements real-time conversion strictly using foundational combinational logic without firmware delay.
Standard Decoders Fail Beyond 9
Standard single BCD-to-7-segment decoders (like 7447) display distorted hex symbols for inputs 10–15.
Dual-Digit Hardware Solution
This project decomposes the 4-bit word into two decimal positions: Tens (0 or 1) and Units (0 through 9).

## Slide 3
SECTION 02 • PROJECT SCOPE
Objectives
Binary-to-Decimal Translation
Map all 16 discrete states ($0000_2$ to $1111_2$) into proper base-10 digits across Tens and Units positions.
Boolean Minimization
Formulate complete truth tables and derive minimal Sum-of-Products (SOP) expressions using Karnaugh maps.
Dual 7-Segment Driving
Interface combinational converter outputs with dual 7447 active-low decoders and common anode displays.
Hardware Prototyping
Validate timing and gate delays in Logisim Evolution, then wire and test a functional 5V TTL circuit on breadboard.

## Slide 4
SECTION 03 • PEDAGOGICAL MAPPING
Course Outcomes (COs) Mapping
CO1:
Apply binary number systems, 8-4-2-1 positional weights, and Boolean algebra to digital circuits.
CO2:
Design combinational circuits through Karnaugh map minimization for specified input-output relations.
CO3:
Implement MSI components including BCD decoders (7447) and sequential D-registers (7474) for stable data routing.
CO4:
Simulate, analyze propagation delay, and troubleshoot digital circuit schematics using CAD tools (Logisim).
CO5:
Demonstrate physical hardware interfacing with breadboards, 7-segment displays, and CPU datapath buses.

## Slide 5
SECTION 04 • BILL OF MATERIALS
Components Required
Digital Integrated Circuits
Displays & Hardware Support
IC 7408 (Qty: 1): Quad 2-input AND gate for product terms
IC 7432 (Qty: 1): Quad 2-input OR gate for sum terms
IC 7404 (Qty: 1): Hex Inverter for complemented inputs
IC 7447 (Qty: 2): BCD to 7-Segment Decoder / Driver
IC 7474 (Qty: 1): Dual D Flip-Flop for registered input sync
7-Segment Displays (Qty: 2): Common Anode LED displays
DIP Switch (4-position): Manual binary input ($B_3, B_2, B_1, B_0$)
Current Limiting Resistors: $14 \times 330\,\Omega$ (for LED segments)
Pull-Down Resistors: $4 \times 10\,\text{k}\Omega$ (for DIP switches)
Power Supply & Chassis: +5V DC regulated supply, breadboard & wires

## Slide 6
SECTION 05 • SYSTEM ARCHITECTURE
Block Diagram
Signal Flow: Binary inputs feed combinational logic to separate the Tens bit from the 4-bit Units BCD code before passing to 7447 active-low decoders.
4-Bit Input
DIP Switch ($B_3 B_2 B_1 B_0$)
Logic Converter
AND / OR / NOT Gates
Dual 7447 Decoders
Tens & Units Decoders
7-Segment Output
Decimal "00" to "15"

## Slide 7
SECTION 06 • THEORY OF OPERATION
Circuit Working Principle
For binary counts 0000 to 1001, value is single-digit. Tens digit is 0 ($T=0$). Units bits pass directly unchanged ($U_3=B_3, U_2=B_2, U_1=B_1, U_0=B_0$).
For counts 1010 to 1111, Tens digit becomes 1 ($T=1$). Combinational logic subtracts 10 ($1010_2$) from the binary input to produce units digits 0 to 5.
Tens BCD (0 or 1) and Units BCD (0–9) enter dual 7447 decoders, driving active-low common anode displays through 330Ω current-limiting resistors.
1
Transparent Zone (0–9)
2
Adjustment Zone (10–15)
3
Segment Drive & Display

## Slide 8
Decimal | B₃ B₂ B₁ B₀ | Tens (T) | U₃ U₂ U₁ U₀ | Output | Decimal | B₃ B₂ B₁ B₀ | Tens (T) | U₃ U₂ U₁ U₀ | Output
0 | 0 0 0 0 | 0 | 0 0 0 0 | "00" | 8 | 1 0 0 0 | 0 | 1 0 0 0 | "08"
1 | 0 0 0 1 | 0 | 0 0 0 1 | "01" | 9 | 1 0 0 1 | 0 | 1 0 0 1 | "09"
2 | 0 0 1 0 | 0 | 0 0 1 0 | "02" | 10 | 1 0 1 0 | 1 | 0 0 0 0 | "10"
3 | 0 0 1 1 | 0 | 0 0 1 1 | "03" | 11 | 1 0 1 1 | 1 | 0 0 0 1 | "11"
4 | 0 1 0 0 | 0 | 0 1 0 0 | "04" | 12 | 1 1 0 0 | 1 | 0 0 1 0 | "12"
5 | 0 1 0 1 | 0 | 0 1 0 1 | "05" | 13 | 1 1 0 1 | 1 | 0 0 1 1 | "13"
6 | 0 1 1 0 | 0 | 0 1 1 0 | "06" | 14 | 1 1 1 0 | 1 | 0 1 0 0 | "14"
7 | 0 1 1 1 | 0 | 0 1 1 1 | "07" | 15 | 1 1 1 1 | 1 | 0 1 0 1 | "15"
SECTION 07 • TABULAR FORMULATION
Truth Table

## Slide 9
SECTION 08 • BOOLEAN EQUATIONS
Logic Design & K-Map Equations
Tens Digit (T)
Units Bit 2 (U₂)
Units Bit 1 (U₁)
Units Bit 0 (U₀)
Active for minterms 10, 11, 12, 13, 14, 15.
Active for minterms 4, 5, 6, 7, 14, 15.
Active for minterms 2, 3, 6, 7, 12, 13.
Direct LSB passthrough without gates.
T = B₃B₂ + B₃B₁ = B₃(B₂ + B₁)
U₂ = B₂B₃' + B₂B₁ = B₂(B₃' + B₁)
U₁ = B₃'B₁ + B₃B₂B₁'
U₀ = B₀ (U₃ = 0 always)

## Slide 10
SECTION 09 • CAD MODELING & TESTING
Simulation / Implementation
Logisim Evolution Simulation
Breadboard Implementation
✓ Built modular 4-bit converter subcircuit block.
✓ Applied automated truth-table test vectors (0000–1111).
✓ Validated 7-segment segment mapping ($a$ to $g$) without illegal glyphs.
✓ Confirmed boundary transition $9 \rightarrow 10$ with zero race conditions.
✓ ICs 7408, 7432, 7404, and 7447 socketed across center IC channel.
✓ Common rails tied to regulated 5.0V DC and system ground.
✓ $330\,\Omega$ current-limiting resistors protected each display segment.
✓ Verified full range 00 through 15 with manual DIP inputs.

## Slide 11
SECTION 10 • SYSTEM BENEFITS
Advantages
Real-Time Speed
Pure combinational translation produces decimal output within propagation delay ($< 25\text{ ns}$) with zero clock cycles.
No Firmware Dependency
Eliminates microcontroller programming, memory footprint, boot time, and code corruption risks.
Low Cost & Simple
Constructed using standard, globally available, inexpensive 74xx TTL series components.
High Educational Value
Provides clear physical intuition on Boolean algebra, K-maps, decoders, and display driving.

## Slide 12
SECTION 11 • ENGINEERING CONSTRAINTS
Limitations
Fixed Input Range (0–15)
Architecture strictly decodes 4 binary bits (0 to 15). Cannot convert numbers $\ge 16$ without redesigning combinational logic or adding shift-add-3 modules.
Wiring & Fan-Out Complexity
Direct gate-level implementation requires 14 current-limiting resistors and dozens of point-to-point breadboard jumper connections.
Switch Contact Bounce
Raw DIP switches create mechanical chatter during toggling, requiring D-register filtering or RC debouncing to prevent display jitter.

## Slide 13
SECTION 12 • REAL-WORLD CONTEXT & UPGRADES
Applications & Future Scope
Current Applications
Future Scope
CPU ALU Output Monitoring: Direct visual debugging of 4-bit accumulator results without firmware interrupt overhead.
Digital Instrumentation: Simple frequency counters, token displays, and industrial sensor readouts.
Educational Demonstration: Lab teaching aid for Boolean algebra and display decoding.
8-Bit / 16-Bit Double Dabble: Expand circuit using cascaded add-3 algorithm blocks for larger binary values (0–255).
FPGA & ASIC Synthesis: Synthesize using Verilog HDL for integration into System-on-Chip (SoC) peripheral modules.
Dynamic Display Multiplexing: Implement high-frequency digit switching using 555 timers to reduce pin count.

## Slide 14
SECTION 13 • SUMMARY OF RESULTS
Conclusion
100% Functionally Verified
The 4-bit binary to decimal converter successfully decoded all 16 states ($0000_2$ to $1111_2$) into distinct decimal displays "00" through "15" in both simulation and breadboard hardware.
Theory to Silicon Bridge
Proved that complex base conversions can be solved entirely via gate-level combinational mapping without a CPU.
Complete Curriculum Coverage
Demonstrated mastery across all course outcomes: binary systems, K-maps, decoders, registers, and CAD verification.

## Slide 15
SECTION 14 • OPEN SOURCE DOCUMENTATION
GitHub Repository
The repository contains all project deliverables, open-source schematic files, and documentation for replication.
├── circuit_schematic.circ (Logisim-Evolution) ├── truth_table_verification.csv ├── poster_a3_expo.html ├── presentation_slides.html └── README.md (Bill of Materials & Pinouts)
Scan to Access Repository
Full documentation, circuit diagrams, and project report.
Project Source Repository
https://github.com/manikanta-2620040001/4bit-binary-decimal-converter

## Slide 16
PROJECT PRESENTATION COMPLETED
Thank You
Questions & Discussion
Guide: Dr. Venkanna Isampalli • Department of Freshman Engineering • Koneru Lakshmaiah Education Foundation
Manikanta 2620040001
Vignesh
2620030101
Ram Charan 2620030241
Praveen 2620080019